## Slide 1: Controller for Distributed Power Processing in Battery Packs
John Miller, researcher
Dr. Satish Ranade, research mentor

## Slide 2: Batteries in Power Systems

## Slide 3: Batteries in Power Systems
Series - add voltage
Parallel - add capacity
Series/parallel - add voltage and capacity
Notes: Laptop batteries usually have good cells, but the one bad cell makes the entire pack worthless.

## Slide 4: The Problem
Lithium Ion battery cells are 3.7 Volts
  120V/3.7V = 33 cells
Cells frequently go bad
  Charging capacity depends of the worst cell
Can be expensive and time consuming to find and replace
  Need to bring the power off line

## Slide 5: What if there was a better way?

## Slide 6: Dual-Active-Bridge

## Slide 7: Dual-Active-Bridge
Step up the voltage of each cell
Charging more efficient
Bad cells easier to replace

## Slide 8: The Problem

## Slide 9: Problems with using a Dual-Active-Bridge
Expensive
  Each cell will need its own DAB
  Circuitry required to drive DAB relatively expensive
Bulky
  Circuits are relatively large
  Can be power hungry

## Slide 10: The Big Picture

## Slide 11: What is done so far
TI DSP based controller and power electronics completed
Transformer development in progress
Further (4x) reduction in footprint

## Slide 12: REU Project
FPGA Based Controller
Integrate with DAB
Cell/Stack sensors/analytics

## Slide 13: FPGA
Altera DE0-CV
VHDL
  Programmable Logic/Circuits

## Slide 14: DE10-Nano
Similar to the DE0-CV
Cyclone V SOC
800MHz Dual-core ARM Cortex-A9 processor
A/D converter, 4-pin SPI interface with FPGA

## Slide 16
ADC
FPGA
DAB
SPI Communication Onboard
PWM Signal Generated
Output Voltage Monitor

## Slide 17: VHDL Design
Pulse Width Modulation (PWM)
  Square wave
  Variable duty cycle
  Variable phase shift
UART Communication
  For sensors
Sensor Feedback
  Calculate modification

## Slide 20: VHDL & Block Diagrams

## Slide 21: PWM Output
if (count_1 = duty_cycle) then
pwm1_out <= '1';
end if;
if (count_1 = clock_ticks) then
pwm1_out <= '0';
end if;
clock_ticks = 1000
duty_cycle

## Slide 22: PWM Output With Inverse
if (count_1 = duty_cycle) then
pwm1_out <= '1';
pwm1_out_bar <= ‘0';
end if;
if (count_1 = clock_ticks) then
pwm1_out <= '0';
pwm1_out_bar <= ‘1';
end if;
clock_ticks = 1000
duty_cycle

## Slide 23: PWM Output With Phase Shift
if phase_2 /= abs (count_1 - count_2) then
count_2 := count_1 + phase_2
end if;
count_1 := count_1 + 1;
count_2 := count_2 + 1;
clock_ticks = 1000
duty_cycle

## Slide 24: PWM Block Diagram
pwm1_out
pwm1_out
pwm2_out
pwm2_out
clk
phase_2
pwm_double

## Slide 25: Auto Phase Shift Block Diagram
phase_shift
clk
phaser_auto

## Slide 26: Top Level Block Diagram
clk
GPIO_1
GPIO_2
phase_shft
clk
ticker_out
phase_2
pwm1_out
pwm1_out_bar
pwm2_out
pwm2_out_bar
phaser_auto
pwm_double
pwm_test
clk

## Slide 27: Phaser Block Diagram
phaser_auto
clk
ticker_out
clk
ticker
ticker1
pwm
pwm
phase_control
clk
clk
clk
pwm_out
pwm_out
pwm_phase

## Slide 28: Phase_control
process(clock)
variable foward : std_logic :='0';
begin
if rising_edge(clock) then
if foward = '0' then
count <= count +1;
elsif foward = '1' then
count <= count - 1;
end if;
if count = max_val-1 then
foward := '1';
elsif count = 1 then
foward :='0';
end if;
end if;
end process;
phase_control
clk
pwm_phase

## Slide 30: Challenges

## Slide 31: Challenges
Change the phase of the PWM Signal
  VHDL will not take default values at startup
  Requires a state to compare startup
Difficult getting analog input
  Limited documentation on ADC
  Software version mismatch with what is available
  Software not working with FPGA correctly

## Slide 37: What’s Next?
Receive analog input into FPGA
  Convert ADC input to integer
  Integer input to PWM “phaser” is working

## Slide 38: Literature

## Slide 39: Overview of Dual-Active-Bridge Isolated bidirectional DC-DC Converter for High-Frequency-Link Power-Conversion System
Overview of Dual-Active-Bridges
Applications and Use
How they work
Methods of Control

## Slide 40: FPGA Prototyping by VHDL Examples
Example projects
UART explanation

## Slide 41: Altera Documentation
ADC Documentation and tutorials

## Slide 42: Questions